## Slide 1: Tutorial 1 combinational logic circuit

## Slide 2: Overview
We will review the following concept in this tutorial:
Combinational logic circuit
  No memory, output(s) solely determined by input(s)
Truth table and logic function
Two-level logic and PLA
Simplification with Boolean Algebra and K-map
Circuit design
Work with two practical examples
  Bit comparator
  Encoder

## Slide 3: Digital Logic Circuit
Two types of digital logic circuits inside a computer:
  Combinational logic circuits
    Logic circuits that do not have memory
    The output depends only on the current inputs and the circuit
    They can be specified fully with a truth table or a logic equation
  Sequential logic circuits
    Logic circuits that have memory
    The output depends on both the current inputs and the value stored in memory (called state)

## Slide 4: Circuit Design Process
A simple logic design process involves
  Problem specification
  Truth table derivation
  Derivation of logical expression
  Simplification of logical expression
  Implementation

## Slide 5: Review of Boolean Algebra
Boolean algebra consists of
  Boolean variables (with values equal to either ‘0’ or ‘1’ )
  Binary operators: AND (∙), OR (+), NOT ( ‘ )
Any logic function can be expressed as a two-level logic expression, either as
  Sum-of-Products (SoP) representation, or
  Product-of-Sums (PoS) representation
The AND, OR, and NOT operations form a functionally complete set (namely, universal gates), as they can specify any logic function.

## Slide 6: Basic Laws of Boolean Algebra

## Slide 7: Boolean Algebra Exercise 1
Find the direct Boolean expression for the following circuit
Simplify the Boolean expression using Boolean algebra
Draw the new circuit for the simplified Boolean expression

## Slide 8: Boolean Algebra Exercise 2
Simplify the combinational logic circuit shown below to a minimum form

## Slide 9: Boolean Algebra Exercise 3
Simplify the following Boolean expression

## Slide 10: 2-bit Comparator Exercise
Here we’ll be designing circuits to compare 2-bit binary numbers.
Suppose we have two 2-bit numbers A & B at the inputs, and three outputs as A>B, A==B, A<B
Only one of the three outputs would be true accordingly if A is greater than or equal to or less than B.
We’ll practice the circuit design for f(A==B), try to work on f(A>B) and f(A<B) by yourself

## Slide 11: 8-to-3 Encoder Exercise
An encoder (2N-to-N encoder) is a logical block with 2N 1-bit inputs and a N-bit output, which performs the inverse function of a decoder.
Example (8-to-3 encoder)
    8 inputs (D0, D1, …, D7) and 3 outputs (X, Y, Z)
Let’s design the circuits for X, Y, Z

## Slide 12: 8-to-3 Encoder Truth Table
D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1

## Slide 13: Extra Exercise: Multiplexor
A multiplexor is a devices that given the control signal, selects one of the inputs to be forwarded to the output. The following figure shows a 4-input multiplexor.
4-to-1 multiplexor

## Slide 14: Questions
If the inputs A/B are 32-bit in width, what is the data width of the Output O?
What is the maximum number of inputs if the control signal is 10-bit in width?
What is the bit-width of the control signal for the multiplexor if there are 9 inputs?